## Slide 1
WORKING AT HEIGHTS
Portable Ladders

## Slide 2
Cracks across
the timber grain
Splits along
the timber grain
Moisture
damage
Burns or charring
Termite
damage
Sheet 1 - Checking timber ladders

## Slide 3
Twisted or deformed
ladder parts
Loose or missing
screws and rivets
Sharp edges and burrs
Metal fatigue and cracks
Corrosion due to
contact with acids
or caustic soda
Sheet 2 - Checking metal ladders

## Slide 4
Loose rungs
Worn or missing
slip resistant feet
Loose or bent
tie rod
300mm spacing
A
Loose or missing
tie rod ends
Stile twisted
or bowed
Even spacing
between stiles
A
Sheet 3 - Checking single type ladders

## Slide 5
Clutch fails
to lock
Condition of
anti-slip feet
Cracked or
loose rungs
Frayed or cut
haul ropes
Bowed stiles
Loose steel wire
or plastic fibre
reinforcing
Twisted stile
Sheet 4 - Checking extension ladders

## Slide 6
Warped or twisted
back leg
Loose batten
screws
Cracked or split
batten
Split or cracked
stile
Loose or split brace
Frayed or cut cords
Seized hinges
Loose top plate
Loose tread or
missing screws
Metal spreader arms should be locked into place when the ladder is fully spread
Sheet 5 - Checking step ladders

## Slide 7
Lashed with rope
to prevent movement
1 metre extension
past the support
point
4m
1m
Ladder set at a
4 to 1 ratio
Stile feet resting
on a firm and level
surface
Sheet 6 - Positioning and securing ladders

## Slide 8
Capacity rating of
120 kilograms
One person at a time on the ladder
Face the ladder when climbing up or down
Use both hands
Three point of contact
Use all rungs
Step onto and off the ladder
Keep your body centred between
the stiles
Don’t reach more than arms
length from the stile
Highest standing
point
Ladders with any metal should not be used near electrical power sources
Sheet 7 - Using a ladder